## Slide 1
OPERATING
SYSTEMS - Advanced
Project
Fagnani Pietro
s303490@studenti.polito.it
D'Elia Luca
s296480@studenti.polito.it
Massetti Marco
s301163@studenti.polito.it
Serra Jacopo
s303510@studenti.polito.it
Emiliano Massimo
s301114@studenti.polito.it
Sineo Gioele
s301398@studenti.polito.it
Year 2023
-
Di Carlo Stefano Carpegna Alessio

## Slide 2
6
1
2
3
4
5
OPERATING
SYSTEMS - Advanced
Project
INTRODUCTION
FINAL CONSIDERATIONS
HARDWARE DESCRIPTION
USER APPLICATION
WORK STEPS
DRIVER APPLICATION

## Slide 3
03
1- Introduction
6
1
2
3
4
5
Development of a Linux device driver for a crypto core in a PYNQ-Xilinx board.
For the development of the driver different steps are required starting from the creation of the hardware accelerator, then to the development of the driver and the user application up to some examples of execution that test the functionality of the entire project.

## Slide 4
04
1- Introduction
1
SHA-1 (Secure Hash Algorithm 1) is a cryptographic hash function that processes input data in blocks, applying mathematical operations and transformations to create a fixed-length 160-bit (20-byte) hash value. This hash value is a unique representation of the input data and is used for data verification and integrity purposes.

## Slide 5
05
1- Introduction
1
Driver applications act as intermediaries between an operating system and hardware components, ensuring effective communication and enabling optimal hardware utilization for users.
The instructions requested by the user through the user application are translated into hardware operations that perform specific functions. This is a necessary job to make custom input/output communicate with the processor or micro-controller used at that time.

## Slide 6
06
1- Introduction
1
The PYNQ-Z2 is a development board designed for embedded systems and digital design projects. The PYNQ-Z2 board features a Xilinx Zynq-7000 system-on-chip (SoC), which combines a dual-core ARM Cortex-A9 processor with programmable logic (FPGA).
To enhance the performance, it's essential to incorporate an independently developed block, known as a Hardware Accelerator.
To connect this block with the CPU of the board an open standard is used developed directly by ARM called AXI4 Interface.

## Slide 7
07
1- Introduction
1
VIVADO and VITIS are used for the success of the following steps:
  The software VIVADO creates the working hardware platform. Is possible specify the card on which you want to load the project. Then the VHDL code is written for the block to be inserted and through the program perform the union of the structures.
  Through VITIS it is possible to connect the hardware component with the CPU through the Bare-Metal CODE. Bare-metal programming refers to programming that interacts with a system at the hardware level, without being filtered by various levels of abstraction.

## Slide 8
08
2- Hardware Description
6
1
2
3
4
5
The hash algorithm is performed on the FPGA.

## Slide 9
09
2- Hardware Description
2
The crypto core that perform the SHA1 algorithm is obtained from the Open Core community (https://opencores.org/projects/sha1).
The core works at the speed of the clock of the FPGA and generate output signals that last only one clock cycle. To manage in a better way the core, an hardware interface wraps it and handles the input/output signals for the CPU.

## Slide 10
10
2- Hardware Description
2
The main component of the hardware accelerator are:
CU: a FSM that manages the whole interface
Registers: hold the data in input and the first CV
CNT and MUX: are used to send in the correct order the input data to the core

## Slide 11
11
2- Hardware Description
2

## Slide 12
12
3- Work Steps
6
1
2
3
4
5
To obtain a working project, specific steps must be followed.

## Slide 13
13
3- Work Steps
3
The remaining steps to the completion of the project are:
  Synthesize the accelerator for the FPGA mounted on board of the PYNQ-Z using VIVADO.
  Use VITIS to generate the interface between the FPGA and the CPU by using bare-metal code.
  Implement the driver function to work with the VFS
  Generate the kernel object with PetaLinux
  Write the user application.
  Compile and then load on the board

## Slide 14
14
4- Driver Application
6
1
2
3
4
5
Without drivers, the OS wouldn't understand how to operate the devices. They serve as translators, converting software commands into hardware actions, ensuring smooth interaction between the two.

## Slide 15
15
4- Driver Application
4
The driver’s files are sha1_driver.h and sha1_driver.c
The implemented functions are:
sha1_open
sha1_read
sha1_write
sha1_ioctl
sha1_release

## Slide 16
16
4- Driver Application
4
sha1_open
sha1_read
sha1_write
sha1_ioctl
sha1_release
This is called whenever a process attempts to open the device file.
The hardware is initialized.
Parameters:
inode: a pointer to an inode object (defined in linux/fs.h)
filep: a pointer to a file object (defined in linux/fs.h)
return: returns 0 if successful

## Slide 17
17
4- Driver Application
4
sha1_open
sha1_read
sha1_write
sha1_ioctl
sha1_release

## Slide 18
18
4- Driver Application
4
sha1_open
sha1_read
sha1_write
sha1_ioctl
sha1_release
This function is called whenever a process which has already opened the device file attempts to read from it.
Starting from the address selected using the ioctl the device registers are readed for the length of the buffer specified as function argument.
Parameters:
file: a pointer to a file object (defined in linux/fs.h)
buffer: the pointer to the buffer to which this function writes the data
length: the length of the buffer
offset: the offset if required
return: returns the number of bytes that have been correctly readed

## Slide 19
19
4- Driver Application
4
sha1_open
sha1_read
sha1_write
sha1_ioctl
sha1_release

## Slide 20
20
4- Driver Application
4
sha1_open
sha1_read
sha1_write
sha1_ioctl
sha1_release
This function is called when somebody tries to write into our device file.
Starting from the address selected using the ioctl the device registers are writen for the length of the buffer specified as function argument. Parameters:
file: a pointer to a file object
buffer: the buffer to that contains the string to write to the device
length: the length of the array of data that is being passed in the const char buffer
offset: the offset if required
return: returns the number of bytes that have been correctly written

## Slide 21
21
4- Driver Application
4
sha1_open
sha1_read
sha1_write
sha1_ioctl
sha1_release

## Slide 22
22
4- Driver Application
4
sha1_open
sha1_read
sha1_write
sha1_ioctl
sha1_release
This function provides commands to the device.
Using this function it is possible to select a register to target for the read/write operations.
Parameters:
file: a pointer to a file object (defined in linux/fs.h)
ioctl_num: a command
ioctl_param: the arguments for the command
return: returns 0 if successful

## Slide 23
23
4- Driver Application
4
sha1_open
sha1_read
sha1_write
sha1_ioctl
sha1_release
This function is called whenever a process attempts to close the device file.
The hardware is resetted.
Parameters:
inode: a pointer to an inode object (defined in linux/fs.h)
filep: a pointer to a file object (defined in linux/fs.h)
return: returns 0 if successful

## Slide 24
24
5- User Application
6
1
2
3
4
5
A program that can use the driver functions to perform a more custom algorithm and obtain an application ready for the user

## Slide 25
25
5
5- User Application
A program that elaborates the data to make it ready for the crypto core is needed.
The algorithm to interface with the user and the driver functions is contained in the files:
main.c
sha1_lib.c
sha1_lib.h
main.c:
The user can decide to perform the hash algorithm on a string or a file. On the user interface is shown the result of the sha1 algorithm.

## Slide 26
26
5
5- User Application
sha1_lib.c and sha1_lib.h:
These files handle the management of the driver device by using the driver's functions and checking for any errors that might occur.
Firstly, the length of the message is observed and the bytes are counted. Subsequently, the message is hashed using the original initialization vector (CV). The content of the first block (512 bits) is read. The process continues with the next block, using the CV created from the previous iteration. At this stage, it is checked whether the last read block requires an additional block for padding. Finally, padding is performed by inserting the right sequence of bits.

## Slide 27
27
5
5- User Application
sha1_lib.c and sha1_lib.h:
Algorithm to split the message into blocks and perform the padding.

## Slide 28
28
5
5- User Application
sha1_lib.c and sha1_lib.h:
Algorithm to send the data to the FPGA.

## Slide 29
29
5
5- User Application
The padding is obtained by appending a 1, followed by enough 0s until the message is 448 bits. Then the length of the message represented by 64 bits is added to the end, producing a message that is 512 bits long. If the last block is longer than 448 bits, then one another block is used to be sure to be able to add the last 64 bits.

## Slide 30
30
6- Final Considerations
6
1
2
3
4
5
Is this project really working? How much is this hashing algorithm safe? How the source-code can be obtained?

## Slide 31
31
6
6- Final Considerations
Example of the successful running of the project:

## Slide 32
32
6
6- Final Considerations
Starting in 2005, the security of the SHA-1 algorithm became uncertain, leading many organizations to seek a replacement. In 2017, researchers from CWI Amsterdam and Google reported a successful collision attack against SHA-1.
The initial attack focused on a simplified version of the algorithm and managed to crack 53 out of 80 rounds using less than computational operations.
In 2015, a significant breakthrough occurred in the field of cryptography. An attack was done against the SHA-1 hash function, requiring only calculations. This was the first successful attempt to hack the full version of the algorithm. This event is widely known as the “SHAppening”.

## Slide 33
33
6
6- Final Considerations
In 2017, Google generated a collision, later named “SHAttered”, that put a definitive end to the SHA-1 algorithm.
The company was able to generate two different .pdf files having the same SHA-1. Analyzing the two files shows that they differ from each other by only a few bytes, but despite this, the attack required an incredible amount of computation, as described in the study's official paper.
https://shattered.io/

## Slide 34
34
6
6- Final Considerations
The source code of the project is distributed on a public GitHUB repository using a CC BY-NC 4.0 license.

## Slide 35
6
1
2
3
4
5
Do you have any question?

## Slide 36
6
1
2
3
4
5
THE END - THANK YOU
FOR THE ATTENTION